## Slide 1
Voltage refs are needed for ADC, LDO, Buck conv, bias circuits

## Slide 4
The current mirror improves supply rejection but the temperature coefficient is still high M1 , M2 also form a voltage mirror since now M1 and M2 also have same current => VG1 and VGS2 should be the same
Since Vg1 = Vg2 => Vs1 = Vs2 = Veb1

## Slide 5
The positive slope Vt can be generated using two diodes which are forwards biased

## Slide 15
Why use a BJT in diode fashion why not a diode directly? Becuase whe n a didoe is used we we need its anode to be connected to GND to forward bias it. In that way the P_Substrate is actually connected to a potential and not to ground which is the usual connection in BiCMOS process node. So to avoid biasing the substrates of the other devices we use a BJT connected in a diode fashion.
Why not option b? Becuase we can see some collector current going through the P substrate which is not supposed to be carrying any current
Why option c? Becuase most of the collector current will not flow through the P+ doped region and not the P substrate of the device

## Slide 16
More info and derivation in the pdf fill attached along with this document

## Slide 17
Other important relationships: If more devices are added in parallel with the BJT then the slope becomes more -ve since more devices => more variation w.r.t to Temperature i.e. dVbe/dT gets added
If Ic is lower => Vbe is lower From the previous eq, dVbe/dT becomes even more -ve

## Slide 18
Current mirror or OPamp or VCVS basically to put a nullator at the input to either match the currents or voltages

## Slide 19
V1 curve will have a more -ve slope because it has lower current flowing through it. Hencce providing a +ve slop for PTAT Also PTAT is actually the voltage output across the R1 resistor

## Slide 20
temperature dependence of the resistance is usually ignored in the PTAT sources

## Slide 21
Now MP1, MP2 and MP3 form a current mirror => I1 = I2 = I3 Since I1 = I2, Vgsmn1 = Vgsmn2, which is the requirement of the PTAT. Hence the first two columns make the PTAT source across R1 i.e. Vptat = I2*R1. Now since I3 = I2 => voltage across R2 is proportional to Vptat and Q3 makes the CTAT. Hence Vref = Vptat + Vctat. The alpha is the factor that can be used to make the slope of Vref w.r.t T = 0

## Slide 24
Initially with Vdd = 0, all currents = 0, when Vdd goesup, assuming there is no startup circuit and hence there are no biasing voltages for any transistor to generate the current and all are off. net 2 will follow Vdd since I2 = 0 and net 1 will remain GND since I1 = 0. This is why a startup circuit is needed.
What does a startup circuit do? net2 = Vdd initially. Since MN3 is always in saturation => it is ON automatically
=> net 6 will be pulled towards GND becasue Mn3 decides its own Vds
=> Mp5 turn onwhen Vgsmp5 >Vt
=> current flows through net1/MN1. Since Mn1 is diode connected => Mn2 turns on as soon as its Vgsmn2 > Vt => net2 is pulled low acc. to Mn2 Vds
=> MP2, MP1 turn on and MP5 turns off since Vnet6 - Vnet2 will not be > Vt
There are few other things to note here. In the beginning, MP5 is off => Vgsmp5 = 0 => MP4 is diode connected in a way and hence current flows through MP4 The current needed provided by MP5 actually comes from MN2. There is a small positive feedback loop here which is triggered by MN3. After trigger i.e.e MP5 is ON, it will increase net1 towards Vdd and turn ON MN2 which in turn provides the current to MP5 to provide the current to MN1

## Slide 25
Most important design choices are R1 and R2. The sizes of the tansistors can be chosen based on the current consumption which in turn will tell us what Vt we can choose. The choice BJTs will not particularly effect the design choice. and ofcourse MP4, MN3 will consume some current so need to keep that in mind